## Slide 1
Incident Classification
Classify 300 lab and pilot-plant incident reports | AI for Data Work
Kritchart Wongwailikhit, Ph.D.

## Slide 2: The task
Sort 300 incident reports by Type and Severity, then check your file online
AI for Data Work
You get
• incident_reports.txt / .xlsx
300 reports, ids 1–300
• the classification rules
• answer templates (.csv, .xlsx)
You decide
For every report:
Type
Injury · Fire · Release · Equipment · Near miss
Severity
High · Medium · Low
You upload
One .csv or .xlsx file
id, type, severity
to the checker website
Pass: both ≥ 95%
All reports are fictional.

## Slide 3: Type: choose one
If more than one type fits, take the first one in the priority order
AI for Data Work
1. Injury
A person was hurt or felt ill: cuts, burns, sprains, broken bones, chemical on the skin or in the eye, or symptoms such as dizziness from breathing vapour - whether or not treatment was needed.
2. Fire
Flame or smoke from burning or smouldering, including a flame that went out by itself. A burning smell with no smoke and no flame is not a fire.
3. Release
Material escaped from where it should be: spills, leaks, drips, weeps, vapour or gas releases (including a gas-detector alarm caused by a leak), steam or compressed air escaping, or liquid poured into the wrong drain. Vapour given off during normal handling (weighing or pouring on the bench) is not a release. Gas or vapour that burns as it comes out (a flame at a leak or at the neck of a flask) counts only as Fire, not also as a release.
4. Equipment
Equipment damaged, broken, failed or tripped, including a safety device that does not work when tested or needed. A safety device that someone has bypassed (for example with a jumper wire) has not failed: see the broken safety rules under Severity.
5. Near miss
Nothing was hurt, burned, released or damaged, but something unsafe happened or was found.
Priority: Injury > Fire > Release > Equipment > Near miss

## Slide 4: Severity: choose one
Check every part of the report and give the highest severity that any part meets, including parts that belong to a lower-priority type.
AI for Data Work
High
• An injury treated beyond first aid (seen by a doctor or nurse, at a clinic or hospital, stitches, or time off work);
• Any chemical in the eye, even if only rinsed at the eyewash;
• Any fire that needed a fire extinguisher, a sprinkler, the fire brigade or an evacuation;
• A release of a hazardous material that is more than 1 L, or that ended up outside containment (on the floor, bench, ground or into a drain or sink), or that set off a gas detector;
• A safety device that did not work when tested or needed (relief valve, trip or interlock, emergency shower, eyewash, fume-hood alarm).
Medium
• Any other injury (first aid only, or no treatment);
• Any other fire (put out without an extinguisher, or went out by itself);
• A release of a hazardous material of 1 L or less, kept inside containment;
• An equipment failure that stopped or held up an experiment or production run;
• A broken safety rule (for any type of report): work without a required permit, no lockout before opening equipment, required PPE not worn, or a safety device bypassed. Only these four count as broken safety rules.
Low
• Anything else, for example: a release of a non-hazardous material; equipment damage with no effect on work (spares, dents, a standby that took over); a near miss where none of the safety rules above was broken.

## Slide 5: Words that decide the label
Read these definitions before you start
AI for Data Work
Hazardous material
Flammable solvents (acetone, toluene, hexane, methanol, ethanol), acids, alkalis (sodium hydroxide, ammonia) and gases picked up by a gas detector. Non-hazardous: any kind of water, steam, steam condensate, compressed air, dilute salt solution and silicone oil.
Containment
A fume hood, spill tray, drip tray or bund.
First aid
Plasters, cold packs, burn gel, rinsing with water (including at a safety shower or eyewash), resting in fresh air, given on the spot.

## Slide 6: Four worked examples
These four are not among the 300 reports
AI for Data Work
Report
Type
Severity
Why
Student burned a finger on hot glassware; held under cold water by the first aider.
Injury
Medium
A person was hurt; first aid only
250 mL of ethanol spilled inside the fume hood; wiped up with spill pads.
Release
Medium
Hazardous, 1 L or less, inside containment
Door seal of a drying oven torn; the oven still holds its temperature.
Equipment
Low
Damage with no effect on work
Student slipped carrying a 2 L bottle of methanol; it broke on the floor; bruised knee, cold pack.
Injury
High
Injury first; the spill (>1 L, on the floor) makes it High

## Slide 7: Read every report carefully
Small words change the label: ask these questions for every report
AI for Data Work
Was anyone hurt or did anyone feel ill?
Was there flame or smoke, or only a smell?
How much was released: mL or L?
Where did it end up: inside containment, or floor, bench, drain?
Extinguisher, sprinkler, fire brigade or evacuation?
Did a safety device fail, or did someone bypass it?
Did the failure stop the work?
Chemical in the eye, or treated beyond first aid?

## Slide 8: Your answer file
.csv or .xlsx, header row id, type, severity, and 300 rows
AI for Data Work
id
type
severity
1
Release
Medium
2
Equipment
High
3
Injury
High
…
…
…
300
Fire
High
Layout example only: not the answers
Rules
• One file, .csv or .xlsx (first sheet only; any sheet name), with a header row and three columns: id, type, severity.
• One row per report: 300 rows, ids 1 to 300, each id once.
• type must be one of: Injury, Fire, Release, Equipment, Near miss.
• severity must be one of: High, Medium, Low.
• Upper or lower case and extra spaces do not matter; the column order does not matter.
• Templates with ids 1–300 are on the website.

## Slide 9: Check your answers online
kwk-golive.github.io/incident-checker
AI for Data Work
Open the website
Type your student ID
and name
Choose your .csv
or .xlsx file
Press
"Check my answers"
You see
• Type % and Severity %
• Both-right %
• The ids with at least one wrong label
(not which label, not the right answer)
Pass mark
Pass: Type ≥ 95% and Severity ≥ 95%
Excellent: both ≥ 99%
Every check is recorded for your teacher.